## Slide 1
Climate Change, Bioenergy and Population Growth as they Stress the Food-Energy-Water Nexus
B.A. McCarl, ChengCheng Fei, Yingqian Yang
Department of Agricultural Economics
Texas A&M University
Presented Shanghai Jiao Tong University
May 2018

## Slide 2: FEW Nexus
Food-Energy-Water Nexus Analysis considers way sectors interact in the food, energy and water space and in cases ways in which actions by some parties in the FEW sectors can benefit total regional welfare.
We are involved in Nexus Analysis in 2 settings
  Nexus analysis under Water scarcity: Limited supply and increasing demand for water are driving Nexus forces
  Nexus Analysis under major bioenergy decisions – US renewable fuel standard and whether we will expand cellulosic ethanol production plus use marginal land
Today I will mainly talk from the first project as that is one I am leading
This material is based upon work supported by the National Science Foundation under Grants addressing Innovations at the Nexus of Food, Energy, and Water Systems numbered 1639327 and 1739977

## Slide 3: FEW Nexus – Water Scarcity
Water Scarcity FEW Nexus Analysis is stressed by evolving climate and population
  Climate
    Increases water demand in form of desired water use per acre, per household, for electrical cooling and for some other industries
    In study area lowers water supplies and increases variability
    In area lowers yields per unit land, lessening food supply
  Population growth
    Increases household and supporting industry water demand.
    Also increases demands for energy and food
Collectively makes Water scarcity worse
  Lowering supply and increasing demand for water plus adding energy and food demands while lowering food supply

## Slide 4: FEW Nexus – Water Scarcity
In our study we examine FEW Nexus actions in the form of new water related sectoral investments and altered operating strategies- we collectively call these projects
We are working on defining projects:
  Agriculture related projects
  Water related projects
  Energy related projects
We also examine who gains and who loses as we feel Compensation and mechanisms to achieve it will be a big issue

## Slide 5
Background on Regional Issues

## Slide 6: Study Region - Geographic & Hydrologic Scope

## Slide 7: Study Region - Geographic & Hydrologic Scope
Water Sources
4 River Basins
5 Aquifers
2 Springs
5 Lakes/Reservoirs
Users
Agriculture
Municipality
Industry
Energy - power plants and fracking)
Recreational
Environmental

## Slide 8: Limited water supply : Rivers
Average precipitation in the region varies from 20 -30 inches (50-75 cm) per year in the ag areas in west to about 40 inches (100 cm) per year in the east
Sufficient flows needed for downstream water use and flows to Estuary to protect fishery and species.
Interaction with ground water
  Springs from Edwards Aquifer provide 30-80% of base flow in eastern river under drought
  Overpumping of groundwater will lower river flows

## Slide 9: Limited water supply : Aquifers
Edwards Aquifer
Source: Edwards Aquifer Website http://www.edwardsaquifer.net/intro.html

## Slide 10: Limited water supply : Edwards Aquifer
Problems
  Limited water supply (recharge)
  Heavy discharge (pumping and
  springs)
  Environment concerns and
  endangered species finding
EAA solution
  Edwards Aquifer Authority (EAA) issued permits to limit pumping and regulated withdraw amount based on water level
  Permit trading is allowed in EAA (water market)

## Slide 11: Stochastic water supply Edwards Aquifer
Chart: Discharge and Recharge
Unit is thousands of acft which is 1,233 cubic meters)

## Slide 12: Stochastic water supply : Aquifers
Chart: Discharge and Recharge (thousands of acft)
Edwards Aquifer does not retain water

## Slide 13: Environmental Issue - Edwards
Aquifer supports Endangered species
Texas Blind Salamander
Fountain Darter
San Marcos Gambusia
San Marcos Salamander

## Slide 14: Carrizo-Wilcox Aquifer Water Level falling
Chart: Well 7708511
In Groundwater Management area 13 covering southern segment of Carrizo-Wilcox Aquifer, desired 2070 condition is no more than 48 feet average drawdown relative to 2012
Chart: Well 7738103
Chart: Well 7702509

## Slide 15
Background on Demand and Population

## Slide 16: Regional Water Usage by Sector - 2015
Chart: Surface Water Usage (149k Acft)
| Municipal | Industrial | Mining | Power Plant | Irrigation | Livestock
 | 68199.5431 | 12419.2607 | 4646.0778 | 28881.6744 | 23673.8087 | 11260.5705
Chart: Ground Water Usage (643k Acft)
| Municipal | Industrial | Mining | Power Plant | Irrigation | Livestock
 | 347888.8745 | 14128.7482 | 47135.0512 | 5356.741 | 210589.5615 | 18603.5287
Heavy water usage by municipal sector
Irrigation uses mainly groundwater

## Slide 17: Rapid Population Growth
Chart: Bexar County Historical and Projected Population (Million)
| 1980 | 1990 | 2000 | 2010 | 2020 | 2030 | 2040 | 2050
 | 988800 | 1185394 | 1392931 | 1714773 | 1950938.4 | 2199550.2 | 2421592.8 | 2634146.4
Chart: South Central Texas Demand Supply and Gap (Million Acft)
| 2020 | 2030 | 2040 | 2050 | 2060 | 2070
Demands | 1070354 | 1156030 | 1219229 | 1290567 | 1366447 | 1433835
Existing Supplies | 1027889 | 1028407 | 1027680 | 1022969 | 1017842 | 1015732
Deficit | 42465 | 127623 | 191549 | 267598 | 348605 | 418103
Population growth leads to
Rapid municipal industrial and electricity cooling demand
Growing deficit

## Slide 18: Challenges from Fracking
Between 2000 and 2014, water used to drill a horizontal natural gas well increased from 177,000 to 5.1 million gallons per well
Fracking (mining) is largest water use in some counties.
Heavy fracking in winter garden increased Carrizo-Wilcox drawdown.
Chart: Mining water usage as proportion of total usage
| 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Dimmit | 0.019043 | 0.022496 | 0 | 0.038067 | 0.017969 | 0.029532 | 0.033985 | 0.078539 | 0.079187 | 0.055077 | 0.060738 | 0.056735 | 0.059153 | 0.068403 | 0.0674 | 0.066725 | 0.00020336 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.010147 | 0.07557 | 0.14494 | 0.30403 | 0.47816 | 0.58322 | 0.58859 | 0.56907
LA Salle | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.01114 | 0.050118 | 0.096004 | 0.22253 | 0.46118 | 0.50611 | 0.64481 | 0.68403
Chart: Water Elevation of Well 7738103 on La Salle and Dimmit Boarder

## Slide 19
Climate Change

## Slide 20: Temperature history
Year | Change from 20th Century Average | Rank out of 138 years
2014 | 0.74°C | 135
2015 | 0.90°C | 137
2016 | 0.94°C | 138
2017 | 0.84°C | 136
2017 was the third warmest year in NOAA's 138-year series.
41ht consecutive year (since 1977) that annual temperature is above 20th century average.
All 17 years of 21st century rank are among seventeen warmest on record (1998 is ninth)
Six warmest years have all occurred since 2010
Four warmest have been last 4
Temperatures in 2015-2016 were majorly influenced by strong El Niño
Increased 0.07°C (0.13°F) per decade since 1880 and 0.17°C (0.31°F) since 1970

## Slide 21: Climate Change is making things non stationary
Chart: Edwards Aquifer Recharge Over Time
| 1934 | 1935 | 1936 | 1937 | 1938 | 1939 | 1940 | 1941 | 1942 | 1943 | 1944 | 1945 | 1946 | 1947 | 1948 | 1949 | 1950 | 1951 | 1952 | 1953 | 1954 | 1955 | 1956 | 1957 | 1958 | 1959 | 1960 | 1961 | 1962 | 1963 | 1964 | 1965 | 1966 | 1967 | 1968 | 1969 | 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Recharge 1934-1975 | 179.6 | 1258.2 | 909.6 | 400.7 | 432.7 | 399 | 308.8 | 850.7 | 557.8 | 273.1 | 560.9 | 527.8 | 556.1 | 422.6 | 178.3 | 508.1 | 200.2 | 139.9 | 275.5 | 167.6 | 162.1 | 192 | 43.7 | 1142.6 | 1711.2 | 690.4 | 824.8 | 717.1 | 239.4 | 170.7 | 413.2 | 623.5 | 615.2 | 466.5 | 884.7 | 610.5 | 661.6 | 925.3 | 756.4 | 1486.5 | 658.5
Recharge 1975-2015 | 658.5 | 973 | 894.1 | 952 | 502.5 | 1117.8 | 406.4 | 1448.4 | 422.4 | 420.1 | 197.7 | 1003.3 | 1153.7 | 2003.6 | 355.5 | 214.4 | 1123.2 | 1508.4 | 2485.7 | 447.6 | 538.1 | 531.3 | 324.3 | 1134.6 | 1142.3 | 437.5 | 614.5 | 1069.4 | 1537.7 | 669 | 2176.1 | 764 | 201.6 | 2162.3 | 212.9 | 210.9 | 813.5 | 112 | 313.5 | 182.6 | 107.2 | 1358.1
http://www.edwardsaquifer.net/data.html

## Slide 22: Climate Change is making things non stationary
Water
Can we use 100 year flood?
Milly, PCD, J. Betancourt, M. Falkenmark, 2008. Climate Change: Stationarity Is Dead: Whither Water Management?, Science, Vol. 319. No. 5863, pp. 573 – 574.
McCarl, Bruce A., Xavier Villavicencio, and Ximing Wu. "Climate change and future analysis: is stationarity dying?." American Journal of Agricultural Economics 90.5 (2008): 1241-1247.
Ag yields
Can we history to assess risk?

## Slide 23: Climate Change is making things non stationary USGS 05054000 RED RIVER OF THE NORTH AT FARGO, ND
https://www.ndsu.edu/fargoflood/images/red_river_of_the_north_raster_plot_august_2014.pdf
Where is the dark Blue?
Note it is more common recently

## Slide 24: Yet more could happen
What could happen
What we have seen so far
Figure 1: Global temperature change and uncertainty. From Robustness and uncertainties in the new CMIP5 climate model projections
Reto Knutti & Jan Sedláček, Nature Climate Change 3, 369–373 (2013) doi:10.1038/nclimate1716,

## Slide 25: Climate Change
    Use data for 2030 and 2090
        Canadian Climate Center Model (CCC)
        Hadley Climate Center Model (HAD)
        Average changes for the 10 year periods
Climate Change Scenarios | Temperature (0F) | Precipitation (Inches)
HAD 2030 | 3.2 | -4.1
HAD 2090 | 9.01 | -0.78
CCC 2030 | 5.41 | -14.36
CCC 2090 | 14.61 | -4.56
Less water in much of Southwest region
(IPCC, WH2 AR5 chapter 3)

## Slide 26: Projections – Edwards Aquifer
Results for EA Recharge Prediction
(% change from the BASE )
Hadley
Canadian
Recharge in Drought Years
-20.59
-
-
29.65
Recharge in Normal Years
-
19.68
-
-
28.99
-
Recharge in Wet Years
-
23.64
-
-
34.42
-
    Municipal Demand
    Forecasted that climate change will increase municipal water demand by 1.5% (HAD) to 3.5% (CCC).

## Slide 27: Climate Change
Edwards Aquifer is vulnerable under climate change, much less recharge under La Nina
Decreasing precipitation in far future makes Groundwater more vulnerable
Chart: Precipitation Changing Rate Under Canadian GCM
| 2015 | 2020 | 2030 | 2040 | 2050 | 2060 | 2070
Precipitation Changing Rate | 1 | 1.023 | 1.07 | 1 | 0.961 | 0.921 | 0.913
Edwards Aquifer Recharge

## Slide 28
Modeling

## Slide 29: EDSIMR – the concept
Unify
  Detailed aquifer hydrologic model
  Regionalized economic Model
  Surface water flow model
  Hydrology embedded in regional economic model via regression (Keith Keplinger dissertation)
Keith O. Keplinger. "An investigation of Dry Year Options for the Edwards Aquifer. " Ph.D. Thesis, TAMU, 1996.
File Number 598 - Keplinger, K.O., and B.A. McCarl, "Regression Based Investigation of Pumping Limits and Springflow Within the Edwards Aquifer", Texas A and M University, 1995.
File Number 829 - Gillig, D., B.A. McCarl, and F.O. Boadu, "An Economic, Hydrologic, and Environmental Assessment of Water Management Alternative Plans for the South-Central Texas Region", Journal of Agricultural and Applied Economics, 33, 1 (April ), 59-78, 2001.

## Slide 30: EDSIMR “System” (and friends/ancestors)
Regional
Crop Mix
input use
Env.
loads
Crop and
Env
Simulators
(EPIC/SWAT)
Runoff
Simulators
(SWAT)
GIS
Non Ag
Resource
Demand
GCMs
Livestock
Data
Simulator Bundle
Pest
Regressions
Groundwater
Simulator
(GAM)
Water
Quality
EDSIMR
SWAT

## Slide 31: EDSIMR – Components Edwards Aquifer Groundwater and River System Simulation Model
What is contained in EDSIMR ?
Simulation Model (GAM)
Springflow, beginning/ending aquifer elevations, pumping
Econometric Model
Springflow/ending = f (beginning, recharge, pumping)
Mathematical Linear Programming
  Components : objective function
  : ag, M&I power and fracking decision variable
  : constraints
  : Surface water Network flow
  : ground water characteristics
  Linkage : Ground Water + Surface Water

## Slide 32
State of Nature
Aquifers
(Edwards, Carrizo-Wilcox, Gulf Coast, Trinity)
Rivers (Nueces, Guadalupe, San Antonio)
Reservoirs (Canyon , ChokeCanyon, ColetoCreek, Lake Corpus Christi, Medina Lake, Lake Texana)
Aquifer Diverters
River Diverters
Return Flows
Evaporation
Aquifer recharge, Depletion, Elevation
River Flows
Water Project Use (Exist and New)
Water Rights, & Markets
New Water Projects (Y/N)
Energy Retrofits
(Y/N)
Modeled Water Demand
Hydrological Processes
Investments
Reuse
Treatment Plants
EDSIMR – the scope

## Slide 33
Cropland
Agricultural Water Use
Electrical Cooling Water
Fracking Water Use
Water Recreation
Hydro-Electric
Municipal Water
Industrial Water Use
Pasture&
Range
Crop Production
Livestock Production
Fresh water
Aquifer Diversion
River Diversion
Water Projects (Exist & New)
Brackish Water
Modeled Water Demand
Reuse
Return Flows
Treatment Plants
Treatment Plants
Environmental
EDSIMR – Demand Scope
Red means we are
Working on adding it

## Slide 34: EDSIMR – Objective function terms
Max Expected Regional Net Benefit
  Agricultural sector => revenues – production cost
  Non-agricultural sector => areas under demand – supply curves
  Power – operations cost and rev from fixed price
  Fracking – operations cost and fixed demand
  Env sector – to be determined
  Project cost and retrofit cost (water, power, fracking)

## Slide 35: EDSIMR – Agriculture Sector Land Modeling
Land Balance:
  Cropland + Pasture <= Total available land
Land Transfer
Land use decisions are made in Stage 1 of the model (CROPACRES and LIVEPROD)
Irrigate via Furrow
Irrigate via Sprinkler
Dryland
Pasture

## Slide 36: EDSIMR – River flow detail
R3
R1
Lake release
Diversion
R2
c
Spring
Discharge
Aquifer
Return flow
New additional
inflow
Add to Lake
Evaporation
Inflow
Outflow
Recharge
Project water
User
Pump ground
Reuse
Diversion
+ Aquifer recharge
+ Evaporation
+ Lake addition
+ Downstream/bay outflow
Upstream inflow
+ New Additional inflow
+ Return flow
+ Spring discharge
+ Lake release
+ Treated reuse
+ Project water
=

## Slide 37: Stochastic Model
Energy and water projects & retrofits, crop mix, herd size, irrigation to dry, dry to pasture
HDry
Wet
DNormal
State of nature specific
Ag & M/I use
Water trades
Water projects flow
Spring flow
Aquifer elevation
Aquifer Storage
Aquifer Storage and River Flow Identity
MDry
MWet
Normal
Dry
HWet
WNormal
Different
Precipitation
& Recharge
under
Different
SONs

## Slide 38
EDSIMR Objective
Expected Net
Benefits
Maximization
areas
under M&I
demand
curves
pumping
delivery costs
Net Ag income from
Irr and dry Crop and
animalproduction
Annual project dev costs - Integer
Crop plant cost
Animal acquisition annual cost
Cost of irr to dry or dry to past
  The objective function is a probabilistically weighted
  across the states of nature to reflect stochastic weather
  Less SON independent costs
M&I
Ag
Water Mkt Transaction costs

## Slide 39: EDSIMR – Agriculture Sector Crop Mix Modeling
Crop Mix Balance
  Crop mix should be a convex combination of historical crop land allocation
  Dryland and Irrigated crops mixes are counted separately

## Slide 40: EDSIMR –Water rights, and Markets
Diversion Constraint:
  Amount of water diverted from river by one permit
  +Sold to others
  -Buy from others
  <= Permitted Capacity

## Slide 41: EDSIMR – Projects Water, Power, Fracking
Integer variables in most cases
Capacity Constraint
  Water from projects <= the project capacity if the project is built.
  0, otherwise
Project capacity may be stochastic
Operating cost per acre foot
Fixed amortzed construction costs per project
State of nature (stage 2) operation
Injection Balance
  Water could only be recovered in the Hdry state
  Water recovered in the Injection projects in Hdry state <= water injected into aquifer in other state of nature

## Slide 42: EDSIMR – Basics of Stochastics
Stochastics
    Temp and precipitation
    Crop Yields and Water Requirements and pest costs
    Livestock stocking rate
    Livestock performance
    M&I demand
    Cooling requirements
    Water available

## Slide 43: EDSIMR – Incorporating Water Markets
Includes friction in mkt ($50 in Edwards)
Water use and
rights
Municipal
Water use and
rights
Agricultural
Water use and
rights
Industrial
Water
Market

## Slide 44: EDSIMR – Basics of Stochastics
Discrete Stochastic Model :9 weather states
2 Stage Decision
Stage 1
    Water and energy projects
    Crop mix
    Livestock numbers
    Initial levels of aquifers and reservoirs
Stage 2
    Crop water use strategy
    Recharge and surface inflows
    Pumping/diversion
    Water flows

## Slide 45: EDSIMR – Conceptual Results
Projects built
Water Use Pattern and Trading
Economic Effect by party
    regional ag farm income + non-ag net surplus
    regional water prices and costs
Hydrologic Effect
    EA elevation at the J-17 well index and river flows
Environmental Effect
    spring flows, river flows, and the Estuary bay flows
Social Effect

## Slide 46
Projects

## Slide 47: WEF Alternatives – a starting point
Irrigation methods and practices Alternative crops
Ag Land to dryland or grazing Removing minimum limits
Degraded water use Crop mix
Dry year option
Water Use of more distant aquifers Injection &recovery
Reservoirs Saline sources
Enhanced recharge Conservation
Reuse Broader markets and leasing
Interbasin transfer
Energy Alternative cooling Coal to Natural Gas
Renewable sources wind solar Import more
Fracking water reuse Fracking technology

## Slide 48: Water Projects Examples
  Out-of-Region Water Project: Vista Ridge
  143 miles pipelines
  Yield: 50,000 acft/yr
  Water cost full operation $1,976 /acft
  Total cost of facility: $493 million
  Pumping Energy: 156,691 MWh/year
  ASR Project: Luiling ASR
  Total cost of facility: $23 million
  Annual cost of water: $1,086 / acft
  Energy Consumption for pumping: 1,617 MWh/year

## Slide 49: Power Plant Retrofit
Boiler retrofit (coal to natural gas)
Cooling retrofit
  (Once-through to Recirculating to Dry-cooling)
Switch to renewable source: Wind, solar and Nuclear.
Add new capacity in or outside region
  Could export water use
  Wind and solar reliability are issue
Retrofit and new capacity cost will be in first stage of the model

## Slide 50: Public Goods Concern
Some Nexus actions will not be adopted by private individuals as they benefit the public not just the individual. In such cases the public may need to get directly involved in adoption.
Water Projects in our projects are public goods

## Slide 51: Compensation Reallocation
When an entity like a Power plant could retrofit to save water but don’t do it because of cost
We need provide subsidy or compensation to the power plants to increase their incentive of cooling and heating retrofit.

## Slide 52
Preliminary Result

## Slide 53: EDSIMR – Example Analysis Objectives
Evaluate the economic and environmental consequences of a set of water management and energy project plans
Determine the “best” mix of water and energy retrofit options for a given demand and environmental constraints
Undertake a comparative assessment of the model “best” set of water management and energy project plans.

## Slide 54: Base run -Agriculture Land
Land transfers from irrigated land to dry land and sprinkler irrigation is preferred to save water even with higher cost.
Few crop lands transfers to pasture
Chart: Cropland Shares
| base | 2015 | 2020 | 2030 | 2040 | 2050 | 2060 | 2070
Dryland | 698926.18 | 712474.1814 | 713072.8496 | 722987.3895 | 712946.0147 | 725167.0224 | 800059.4103 | 887065.4712
Furrow | 183250.24 | 33050.716 | 33114.1793 | 22323.7821 | 33050.7209 | 24286.7663 | 4268.27 | 10803.776
Sprinkler | 172169.4 | 308688.3626 | 308026.2311 | 308902.0884 | 308216.5243 | 304759.4713 | 249885.5797 | 156344.0128
Chart: Crop Land vs Pasture
| base | 2015 | 2020 | 2030 | 2040 | 2050 | 2060 | 2070
cropland | 1.0543 | 1.0542 | 1.0542 | 1.0542 | 1.0542 | 1.0542 | 1.0542 | 1.0542
Pasture | 13.6631 | 13.6632 | 13.6632 | 13.6632 | 13.6632 | 13.6632 | 13.6632 | 13.6632

## Slide 55: Agriculture Production Index
Chart: Ag Production Index
| 2015 | 2020 | 2030 | 2040 | 2050 | 2060 | 2070
All Ag Products | 1 | 1.1743 | 1.186 | 0.99811 | 0.9238 | 0.95214 | 1.0133
Vegetable | 1 | 3.2764 | 3.786 | 1.0231 | 0.12217 | 0.16761 | 0.54016
Field Crops | 1 | 0.99296 | 1.0122 | 0.99077 | 0.98074 | 1.0041 | 1.1462
Livestock | 1 | 0.91169 | 0.79249 | 1.002 | 1.0406 | 1.0715 | 0.94693
Precipitation | 1 | 1.0235 | 1.0702 | 1 | 0.96064 | 0.92128 | 0.91278
Vegetable production is very sensitive to precipitation. It is preferred during wet years (2020s, 2030s) but spurned in the dry years (2050s, 2060s).
Production index of all ag products also varies with precipitation.

## Slide 56: Water Source by Sector
Demand increases over time with the growing population.
Municipal water needs driving expensive water projects proposed by Texas Water Development Board, or being implemented.
Municipal sector owns less surface water permits than agriculture and industrial sector in the region. Plus has means of financing.
Industrial water relies more on surface water over time, due to the shortage of water projects and groundwater drawdown
Chart: Municipal Water Source
| 2015 | 2020 | 2030 | 2040 | 2050 | 2060 | 2070
Surface | 64.3127 | 40.68 | 45.5331 | 47.9747 | 66.9277 | 100.2238 | 60.2202
Ground | 388.7732 | 423.6383 | 479.5602 | 534.2598 | 568.5323 | 589.7158 | 706.773
project | 0 | 7.0312 | 9.7796 | 9.7146 | 9.6826 | 12.7713 | 23.3978
Chart: 
| 2015 | 2020 | 2030 | 2040 | 2050 | 2060 | 2070
Surface
Ground
Project
Chart: Industrial Water Source
| 2015 | 2020 | 2030 | 2040 | 2050 | 2060 | 2070
Surface | 50.3575 | 49.3837 | 53.9243 | 57.4951 | 55.682 | 60.9394 | 65.5951
Ground | 7.0152 | 11.4137 | 8.7349 | 8.8246 | 21.183 | 19.7137 | 29.3244
project | 0 | 0 | 0 | 0 | 0 | 0 | 0

## Slide 57: Water Source by Sector
Agriculture use less water under climate change, because the increasing demand of groundwater draw down the aquifer and make the water too expensive for agriculture usage.
Mining relies on ground water due to the shortage of surface water permits
Chart: Agriculture Water Source
| 2015 | 2020 | 2030 | 2040 | 2050 | 2060 | 2070
Surface | 76.7287 | 76.8947 | 76.701 | 76.0707 | 72.1246 | 56.87 | 39.1336
Ground | 218.8343 | 248.9675 | 234.9117 | 210.7161 | 191.755 | 153.0321 | 145.453
Chart: Mining Water Source
| 2015 | 2020 | 2030 | 2040 | 2050 | 2060 | 2070
Surface | 4.782 | 4.7826 | 4.782 | 4.782 | 4.794 | 4.716 | 4.7905
Ground | 44.6724 | 44.301 | 44.7463 | 44.8452 | 44.23 | 43.9015 | 44.4241
Chart: 
| 2015 | 2020 | 2030 | 2040 | 2050 | 2060 | 2070
Surface
Ground

## Slide 58: Average Water Cost by Sector
Chart: 
| 2015 | 2020 | 2030 | 2040 | 2050 | 2060 | 2070
Surface
Ground
Project
Chart: Municipal Water Cost
| 2015 | 2020 | 2030 | 2040 | 2050 | 2060 | 2070
Surface | 1659.9672 | 1579.6842 | 1573.0668 | 1535.0901 | 1598.9769 | 1580.8621 | 1510.435
Ground | 1720.4293 | 1722.8227 | 1733.3374 | 1744.8918 | 1749.7308 | 1772.7939 | 1774.7244
project | 0 | 2838.7135 | 2664.6849 | 2272.8252 | 2272.8534 | 2169.1298 | 3049.197
Chart: Industrial Water Cost
| 2015 | 2020 | 2030 | 2040 | 2050 | 2060 | 2070
Surface | 1486.1062 | 1486.0424 | 1487.4974 | 1489.1512 | 1359.7558 | 1338.2851 | 1403.6026
Ground | 1800.8009 | 1992.8602 | 2136.3311 | 2024.7964 | 1638.065 | 1772.5265 | 1725.4773

Chart: Agricultural Water Cost
| 2015 | 2020 | 2030 | 2040 | 2050 | 2060 | 2070
Surface | 10.8538 | 10.8527 | 10.8524 | 10.8535 | 10.2566 | 10.7375 | 10.6103
Ground | 18.227 | 22.2388 | 30.7598 | 40.4903 | 40.5454 | 36.4685 | 48.8049
Chart: Mining Water Cost
| 2015 | 2020 | 2030 | 2040 | 2050 | 2060 | 2070
Surface | 1900.4382 | 1900.3897 | 1900.4382 | 1900.4382 | 1899.4469 | 1900.0245 | 1899.7365
Ground | 1957.8654 | 1958.4005 | 1962.2742 | 1960.7044 | 1968.6918 | 1981.425 | 1977.3748

## Slide 59: Water Projects Selection
 | Available Projects | 2015 | 2020 | 2030 | 2040 | 2050 | 2060 | 2070
Surface Water Projects | 4 |  |  |  |  |  |  | 
Ground Water Projects | 34 | 0 | 4 | 5 | 5 | 5 | 5 | 6
Aquifer Storage and Recovery | 7 | 0 | 2 | 2 | 2 | 2 | 2 | 2
Off-Channel Reservoir | 5 |  |  |  |  |  |  | 
Outside Water Projects | 7 |  |  |  |  |  |  | 
Fixed cost(Million $) |  |  | 3.87 | 3.89 | 0.02 |  |  | 17.60
Variable cost(Million $) | 0 | 0.00 | 29.18 | 35.28 | 35.17 | 35.12 | 40.82 | 72.69
Energy Consumption(MWh) |  |  | 3152 | 4274 | 4267 | 4263 | 5835 | 20220

## Slide 60: EDSIMR – Sample Analysis Results
There is a distinct tradeoff in the EA region between the economic well being of pumping users and regional environmental attributes.
Leaving behind the rule of capture to take on the highest of the HCP motivated pumping limits reduces regional pumping user related welfare by $246 million per year. The most extreme limit examined (175,000 acft) under the emerging HCP raises the welfare loss to $633 million per year.
The emergence of the EA water market improves regional welfare to pumping users but worsens environmental attributes unless the East-West pools could somehow be factored into its design.
Water development from alternative sources will be stimulated greatly by HCP related EA use restrictions.
The EA region will have to develop an expanded set of water development alternatives if the severe Habitat Conservation Plan based restrictions are imposed.

## Slide 61: EDSIMR – Sample Analysis Results
  The EA ag sector is worse off.
  The economic gain accrues to the EA non-agricultural sector, but is basically offset by the water development costs.
Gillig, D., B.A. McCarl, and F.O. Boadu, "An Economic, Hydrologic, and Environmental Assessment of Water Management Alternative Plans for the South-Central Texas Region", Journal of Agricultural and Applied Economics, 33, 1 (April), 59-78, 2001.

## Slide 62: EDSIMR – Sample Analysis Results

## Slide 63: Conclusion
Agriculture transfer land from furrow irrigation to sprinkler irrigation to dryland to save fresh water and avoid high pumping cost
Building more water projects could destress water scarcity and increase social welfare.
More water projects are built over time. ASR and Groundwater projects are preferred due to extra water source and lower fixed and operating cost

## Slide 64: Future Research
Enhance the preliminary electrical energy part improving data and modeling on cooling alternatives and the use of electricity when developing the water projects
Add Edwards Aquifer Authority water management strategies/regulation and water marketing into the model.
Add alternative strategies via which fracking can reduce its usage of fresh water
Develop information on how water supply, crop yield and irrigated crop water use are affected by climate change scenarios in interaction with the SWAT, hydrological modeling group.

## Slide 65: Acknowledgement
This material is based upon work partially supported by the National Science Foundation under Grant Addressing Decision Support for Water Stressed FEW Nexus Decisions Numbered 1739977