## Slide 1: FEW Nexus Water Scarcity
Chengcheng Fei
Bruce McCarl
Yingqain Yang
Department of Agricultural Economics
Presentation at Department Seminar
April, 20, 2018

## Slide 2: FEW Nexus in Our Study
Food-Energy-Water Nexus Analysis considers way actions by some parties in the FEW sectors can benefit total regional welfare.
Water scarcity: Limited supply and increasing demand for water are driving Nexus forces in our study
Economic Concerns: Transaction cost, Public goods, compensation
FEW Nexus actions : new water related sectoral investments and altered operating strategies which we collectively call projects
We are working on defining projects:
  Agriculture related projects
  Water related projects
  Energy related projects

## Slide 3: Study Region Geographic & Hydrologic Scope
Water Sources
4 River Basins
5 Aquifers
2 Springs
5 Lakes/Reservoirs
Users
Agriculture
Municipality
Industries (including power plants and fracking)
Recreationalists
Environmentalists

## Slide 4: Limited water supply : Rivers
The precipitation in the research region varies from 8-20 inches per year in the west to 30-50 inches per year in the east
Sufficient flows needed for downstream water use and flows to Estuary to protect fishery and species.
Interaction with ground water
  Springs
  Overpumping of groundwater will lower river flows (not involved in the model now)
River Authority: Division Permits
Annual precipitation map (1981-2010)
Source: twdb

## Slide 5: Limited water supply : Aquifers
Problems
  Limited water supply (recharge)
  Heavy discharge (pumping and springs)
  Environment concerns and endangered species finding
EAA solution
  Edwards Aquifer Authority (EAA) issued permits to limit pumping and regulated withdraw amount based on water level
  Permit trading is allowed in EAA (water market)

## Slide 6: Limited water supply : Aquifers
Edwards Aquifer
Source: Edwards Aquifer Website http://www.edwardsaquifer.net/intro.html

## Slide 7: Stochastic water supply : Aquifers
Chart: Edwards Aquifer
Edwards Aquifer does not retain water

## Slide 8: Environmental Awareness
Increase Environmental Awareness (Edwards Aquifer)
 Endangered species
Texas Blind Salamander
Fountain Darter
San Marcos Gambusia
San Marcos Salamander

## Slide 9: Edwards Aquifer Regulation

## Slide 10: Water Usage by Sector in 2015
Chart: Region L Surface Water Usage (Acft)
| Muni_SW | MFG_SW | Mining_SW | Power_SW | Irrig_SW | Livestock_SW
 | 58119 | 51217 | 3987 | 26827 | 25247 | 11260
Chart: Region N Surface Water Usage
| Muni_SW | MFG_SW | Mining_SW | Power_SW | Irrig_SW | Livestock_SW
 | 76368 | 41955 | 578 | 2059 | 1042 | 1334
Chart: Region L Groundwater Usage (Acft)
| Muni_GW | MFG_Gw | Mining_GW | Power_GW | Irrig_GW | Livestock_GW
 | 337456 | 14218 | 42296 | 5796 | 208774 | 17266
Chart: Region N Ground Water Usage
| Muni_GW | MFG_Gw | Mining_GW | Power_GW | Irrig_GW | Livestock_GW
 | 15801 | 4484 | 6290 | 0 | 11983 | 3938
Heavy water usage by municipal sector in both region
Region L has heavy irrigation demand
Region L relies more on groundwater
L
N

## Slide 11: Municipal Sector
Chart: Bexar County Municipal Water Use (AcreFeet per Capita)
| 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Munpercapita | 0.23071 | 0.2059 | 0.20414 | 0.1952 | 0.21258 | 0.21131 | 0.19034 | 0.17409 | 0.17236 | 0.16817 | 0.17446 | 0.17696 | 0.17666 | 0.17023 | 0.16953 | 0.17892 | 0.17248 | 0.16976 | 0.15443 | 0.15612 | 0.14887 | 0.17292 | 0.1754 | 0.14746 | 0.17247 | 0.16254 | 0.14716 | 0.16337 | 0.14817 | 0.14274 | 0.1398 | 0.15624
Municipal water use per capita is relatively stable over time
Municipal total water use will increase with population booming in this region
It is hard to reduce demand (Conservation and Education might help to reduce water demand)
Chart: Bexar County Historical and Projected Population
| 1980 | 1990 | 2000 | 2010 | 2020 | 2030 | 2040 | 2050
 | 988800 | 1185394 | 1392931 | 1714773 | 1950938.4 | 2199550.2 | 2421592.8 | 2634146.4

## Slide 12: Fracking
Between 2000 and 2014, water used to drill a horizontal natural gas well increased from 177,000 to 5.1 million gallons per well
Fracking (mining) is largest water use in some counties.
Heavy fracking in winter garden increased Carrizo-Wilcox drawdown.
Chart: Mining water usage as proportion of total usage
| 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Dimmit | 0.019043 | 0.022496 | 0 | 0.038067 | 0.017969 | 0.029532 | 0.033985 | 0.078539 | 0.079187 | 0.055077 | 0.060738 | 0.056735 | 0.059153 | 0.068403 | 0.0674 | 0.066725 | 0.00020336 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.010147 | 0.07557 | 0.14494 | 0.30403 | 0.47816 | 0.58322 | 0.58859 | 0.56907
LA Salle | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.01114 | 0.050118 | 0.096004 | 0.22253 | 0.46118 | 0.50611 | 0.64481 | 0.68403

## Slide 13: Carrizo-Wilcox Aquifer Lift Increase (water level falling)
In Groundwater Management area 13 covering southern segment of Carrizo-Wilcox Aquifer, desired 2070 condition is no more than 48 feet average drawdown relative to 2012

## Slide 14: Economic Concerns

## Slide 15: Major Obstacle and solutions
No enough information or benefit for water conversation
Transaction cost is too high
Public goods concern/ no public activities
Regulation constraint
Build water market and increase conversation
Increase public activities
Relax legislative requirement

## Slide 16: Increase Social Benefit
Much Nexus work arises from a basic assumption that we can increase social benefits by better managing the resources involved. Economics can be used to evaluate whether decisions achieve benefit increases.
We define projects (Agriculture/water/energy related) to achieve the overall increase of social benefit.
This will be discussed later

## Slide 17: Water Value in Diff Market
Water has different value in different uses and this needs both quantification and consideration when making decisions.
Concerns:
  Water movement costs
  Water allocation patterns between users
  Regulation
We will build water market to achieve this goal

## Slide 18: Public Goods Concern
Some Nexus actions will not be adopted by private individuals as they benefit the public not just the individual. In such cases the public may need to get directly involved in adoption.
Water Projects in our projects is public goods

## Slide 19: Externalities
Nexus actions can cause negative impacts or externalities on other parties that need to be taken into account. Social justice is a concern when Nexus actions negatively affects disadvantaged populations.
Example: Pollution caused by fertilizer and fossil power plant

## Slide 20: Compensation Reallocation
Power plant Retrofit to save water
We need provide subsidy to the power plants to increase their incentive of cooling and heating retrofit.
Details will be discussed later

## Slide 21: Projects

## Slide 22: Nexus Projects/Strategies Agriculture Sector
Halt irrigation moving land to dryland or pasture
Sell water in market
Deficit irrigation
Alter crop mix
Irrigation using brackish or saline water (not included in the model now)
Relax legislative requirement for retained water

## Slide 23: Nexus Projects/Strategies Regional Water Projects (mainly M&I)
Regional water planning group identified possible projects in regional water plan. The major classes of these water projects include:
  Build new reservoirs
  Transmit surface and groundwater via pipelines from other regions (mainly ground)
  Desalinate brackish groundwater
  Store mainly flood waters in aquifers for later recovery (ASR)
  Desalinate seawater
  Augment reuse
Electricity consumption by some of these water projects is large
  SAWS Seawater desal would use over 0.1 million MWh per year for pumping only.
  Desal consumption: 3-4.3 MWh/acft (AMTA, 2016) and SAWS seawater desal project is 84,012 acft
Net electricity generation in Region L was 46 million MWh in 2015
Total net electricity generation in Texas is 450 million MWh in 2015

## Slide 24: Water project - Groundwater Transmission
Transfer groundwater via pipeline
Vista Ridge Project
  From Burleson County to SAWS
  143 miles pipelines
  Yield: 50,000 acft/yr
  Water cost full operation $1,976 /acft
  Total cost of facility: $493 million
  Pumping Energy: 156,691 MWh/year
Trinity Groundwater for New Braunfels
  Yield : 1,090 acft/yr
  Annual water cost : $634 / Acft
  Total cost of facility: $4 million
  Pumping Energy: 810 MWh/year

## Slide 25: Water Project - Aquifer Storage and Recovery
Luling ASR
  When surface water exceeds customer demands, and there is unused aquifer storage then surplus water diverted to injection wells for storage.
  When surface water supplies are scarce a blend of treated surface water and recovered water from aquifer wells would be delivered
  Total cost of facility: $23 million
  Annual cost of water: $1,086 / acft
  Energy Consumption for pumping: 1,617 MWh/year

## Slide 26: Water Project - Aquifer Storage and Recovery
Broad Advantages:
  Store excess flows for later use
  Provide supply during drought,
  Meet seasonal demands when use restrictions are imposed,
  Meet demands at the ends of the distribution system
  Provide an emergency supply
  Minimize construction of new facilities and their environmental impacts
Disadvantages:
  Leakage (Edwards: high leakage and brackish; Trinity: high leakage)
  Cannot prevent usage from other users, if the water is stored in the aquifer

## Slide 27: Water Project Build new reservoirs
The Guadalupe-Blanco River Authority (GBRA) Mid-Basin Water Supply Project (MBWSP)
Off-channel reservoir to store flood water.
Capacity: 40,000 acft.
Water cost: $2,561/acft
Pipelines: 31.4 miles
Total cost of facility: $405,562,000
Energy consumption by pumping: 31,158 MWh

## Slide 28: Water Project Desalinate brackish groundwater
Brackish Wilcox Aquifer Groundwater for Sutherland Springs Water Supply Corporation (SSWSC)
Annual Water Cost: $2,554/acft
Yield: 1120 acft/year
Total cost of facility: $12 million
Pumping energy: 392 MWh/year

## Slide 29: Water Project Seawater Desalination
Seawater Desalination for SAWS
The strategy will be a large-scale desalination plant with capacity of 84,012 acft/yr drawing saline water from San Antonio Bay then treated and pumped for delivery to San Antonio Water System
Annual cost: $1,766 / acft
Total cost of facilities: $1.07 billion
Pipeline: 162 miles
Pumping Energy:148,260 MWh/year

## Slide 30: Nexus Projects/Strategies Power Plant Retrofits
Boiler retrofit (coal to natural gas) – need to get water consequences
Cooling retrofit (Once-through to Recirculating to Dry-cooling)
Switch to reusable source: Wind, solar and Nuclear.
Add new capacity in or outside region
  Could export water use
  Wind and solar reliability are issue
Retrofit and new capacity cost will be in first stage of the model

## Slide 31: Power Plant water consumption and costs
 | Water withdrawn and consumption (Gallons per MWh) |  |  |  |  |  | Construction cost per KW | Generation Cost per MWh | Fuel cost per MWh
 | Once-through |  | Recirculating |  | Dry-cooling |  |  |  | 
 | Withdrawal | Consumption | Withdrawal | Consumption | Withdrawal | Consumption |  |  | 
Coal (conventional) | 20,000 - 50,000 | 100 - 317 | 500 - 1,200 | 480 - 1,100 | N/A | N/A | $2934-6600 | $8-17 | ~$30
Natural gas (combined cycle) | 7,500 - 20,000 | 20 - 100 | 150 - 283 | 130 - 300 | 0 - 4 | 0 - 4 | $676-7108 | $5-43 | ~$41
Nuclear | 25,000 - 60,000 | 100 - 400 | 800 - 2,600 | 600 - 800 | N/A | N/A | $5530 | $12.79 | 
Solar thermal (trough) | N/A | N/A | 725 - 1,109 | 725 - 1,109 | 43 - 79 | 43 – 79 | $3873-5067 | $2.82-7.68 | 
Source: Macknick, Jordan, Robin Newmark, Garvin Heath, and Kathleen C. Hallett. "Operational water consumption and withdrawal factors for electricity generating technologies: a review of existing literature." Environmental Research Letters7, no. 4 (2012): 045802. Summarized by Union of Concerned Scientists |  |  |  |  |  |  | EIA, https://www.eia.gov/outlooks/capitalcost/ |  | 

## Slide 32: Cooling Retrofit Cost
 | Capital cost (once-through to recirculating) ($/kW) | Capital cost (once-through or recirculating to dry) ($/kW) | Capital cost (once-through to recirculating) ($/kW) | Capital cost (once-through or recirculating to dry) ($/kW) | O&M cost (once-through to recirculating) ($/kW/yr.) | O&M cost (once-through to dry) ($/kW/yr.) | O&M cost (recirculating to dry) ($/kW/yr.)
 | Average difficulty retrofits |  | Difficult retrofits |  | All retrofits |  | 
Coal | 90 | 220 | 140 | 330 | 2 | 5 | 3
Natural gas combined cycle | 40 | 170 | 65 | 270 | 2 | 10 | 8
Nuclear | 90 | 220 | 140 | 330 | 2 | 5 | 3
Biopower/biogas | 90 | 220 | 140 | 330 | 2 | 5 | 3
Oil/gas simple cycle | 90 | 220 | 140 | 330 | 2 | 5 | 3
Geothermal | N/A | 170 | N/A | 270 | N/A | N/A | 2
Concentrating Solar power | N/A | 170 | N/A | 270 | N/A | N/A | 2

## Slide 33: Other considerations
Water cost is just a small proportion of power plant cost. We may have to consider cost sharing from other parties to get power plants to retrofit.
Water projects increase the electricity demand significantly, if they are applied. Will increase need for more power production / capacity as well as population growth
Build new power plant? High cost, maybe more water usage, increased cost to consumers.

## Slide 34: EDSIMR “System” (and friends/ancestors)
Regionalizing
Model
Regional
Crop Mix
input use
Env.
loads
Crop and
Env
Simulators
(EPIC/SWAT)
Runoff
Simulators
(SWAT)
GIS
Non Ag
Resource
Demand
GCMs
Livestock
Data
Simulator Bundle
Pest
Regressions
Groundwater
Simulator
(GAM)
Water
Quality
EDSIMR
SWAT

## Slide 35
State of Nature
Aquifers
(Edwards, Carrizo-Wilcox, Gulf Coast, Trinity)
Rivers (Nueces, Guadalupe, San Antonio)
Reservoirs (Canyon , ChokeCanyon, ColetoCreek, Lake Corpus Christi, Medina Lake, Lake Texana)
Aquifer Diverters
River Diverters
Return Flows
Evaporation
Aquifer recharge, Depletion, Elevation
River Flows
Water Project Use (Exist and New)
Water Rights, & Markets
New Water Projects (Y/N)
Energy Retrofits
(Y/N)
Modeled Water Demand
Hydrological Processes
Investments
Reuse
Treatment Plants
EDSIMR – the scope

## Slide 36
Cropland
Agricultural Water Use
Electrical Cooling Water
Fracking Water Use
Water Recreation
Hydro-Electric
Municipal Water
Industrial Water Use
Pasture&
Range
Crop Production
Livestock Production
Fresh water
Aquifer Diversion
River Diversion
Water Projects (Exist & New)
Brackish Water
Modeled Water Demand
Reuse
Return Flows
Treatment Plants
Treatment Plants
Environmental
EDSIMR – demand scope
Red means we are
Working on adding it

## Slide 37: Acknowledgement
This material is based upon work partially supported by the National Science Foundation under Grant Addressing Decision Support for Water Stressed FEW Nexus Decisions Numbered 1739977