## Slide 1
Economics of possible welfare increasing energy sector decisions in water stressed regions
Chengcheng Fei, Yingqian Yang, B.A. McCarl
Department of Agricultural Economics
Texas A&M University
Presented at TAMU Conference on Energy
Sep 25, 2018

## Slide 2: FEW Nexus
Food-Energy-Water Nexus Analysis considers way sectors interact in the food, energy and water space and in cases ways in which actions by some parties in the FEW sectors can benefit total regional welfare.
We are involved in Nexus Analysis in 2 settings
  Nexus analysis under Water scarcity: Limited supply and increasing demand for water are driving Nexus forces
  Nexus Analysis under major bioenergy decisions – US renewable fuel standard and whether we will expand cellulosic ethanol production plus use marginal land
Today we will focus on the first project and the impact of Nexus on energy sector, as that is the one we started at

## Slide 3: FEW Nexus – Water Scarcity
Water Scarcity FEW Nexus Analysis is stressed by evolving climate and population
  Climate
    Increases water demand per acre, per household, for electrical cooling , other industries
    In study area lowers water supplies and increases variability
    In area lowers yields per unit land, lessening food supply
  Population growth
    Increases household and supporting industry water demand.
    Increases household and supporting industry electricity demand.
    Also the increases demand of food
Collectively makes Water scarcity worse
  Lowering water supply and increasing demand plus adding energy and food demands while lowering food supply

## Slide 4: FEW Nexus – Water Scarcity
In our study we examine FEW Nexus actions in the form of new water related sectoral investments and altered operating strategies- we collectively call these projects
We are working on defining projects:
  Agricultural related projects
  Water related projects
  Energy related projects
We also examine who gains and who loses as we feel compensation and mechanisms to achieve it will be a big issue

## Slide 5
Background on Regional Issues

## Slide 6: Study Region - Geographic & Hydrologic Scope

## Slide 7: Study Region - Geographic & Hydrologic Scope
Water Sources
4 River Basins
5 Aquifers
2 Springs
5 Lakes/Reservoirs
Users
Agriculture
Municipality
Industry
Energy - power plants and fracking)
Recreational
Environmental

## Slide 8: Limited water supply : Aquifers
Edwards Aquifer
Source: Edwards Aquifer Website http://www.edwardsaquifer.net/intro.html

## Slide 9: Limited water supply : Rivers
Average precipitation in the region varies from 20 -30 inches (50-75 cm) per year in the ag areas in west to about 40 inches (100 cm) per year in the east
Sufficient flows needed for downstream water use and flows to Estuary to protect fishery and species.
Interaction with ground water
  Springs from Edwards Aquifer provide 30-80% of base flow in eastern river under drought
  Overpumping of groundwater will lower river flows

## Slide 10: Limited water supply : Edwards Aquifer
Problems
  Limited water supply (recharge)
  Heavy discharge (pumping and
  springs)
  Environment concerns and
  endangered species finding
EAA solution
  Edwards Aquifer Authority (EAA) issued permits to limit pumping and regulated withdraw amount based on water level
  Permit trading is allowed in EAA (water market)

## Slide 11: Stochastic water supply Edwards Aquifer
Chart: Discharge and Recharge
Unit is thousands of acft which is 1,233 cubic meters)

## Slide 12: Stochastic water supply : Aquifers
Chart: Discharge and Recharge (thousands of acft)
Edwards Aquifer does not retain water

## Slide 13: Environmental Issue - Edwards
Aquifer supports Endangered species
Texas Blind Salamander
Fountain Darter
San Marcos Gambusia
San Marcos Salamander

## Slide 14: Carrizo-Wilcox Aquifer Water Level falling
Chart: Well 7708511
In Groundwater Management area 13 covering southern segment of Carrizo-Wilcox Aquifer, desired 2070 condition is no more than 48 feet average drawdown relative to 2012
Chart: Well 7738103
Chart: Well 7702509

## Slide 15
Background on Demand and Population

## Slide 16: Regional Water Usage by Sector - 2015
Chart: Surface Water Usage (149k Acft)
| Municipal | Industrial | Mining | Power Plant | Irrigation | Livestock
 | 68199.5431 | 12419.2607 | 4646.0778 | 28881.6744 | 23673.8087 | 11260.5705
Chart: Ground Water Usage (643k Acft)
| Municipal | Industrial | Mining | Power Plant | Irrigation | Livestock
 | 347888.8745 | 14128.7482 | 47135.0512 | 5356.741 | 210589.5615 | 18603.5287
Heavy water usage by municipal sector
Irrigation uses mainly groundwater

## Slide 17: Rapid Population Growth
Chart: Bexar County Historical and Projected Population (Million)
| 1980 | 1990 | 2000 | 2010 | 2020 | 2030 | 2040 | 2050
 | 988800 | 1185394 | 1392931 | 1714773 | 1950938.4 | 2199550.2 | 2421592.8 | 2634146.4
Chart: South Central Texas Demand Supply and Gap (Million Acft)
| 2020 | 2030 | 2040 | 2050 | 2060 | 2070
Demands | 1070354 | 1156030 | 1219229 | 1290567 | 1366447 | 1433835
Existing Supplies | 1027889 | 1028407 | 1027680 | 1022969 | 1017842 | 1015732
Deficit | 42465 | 127623 | 191549 | 267598 | 348605 | 418103
Population growth leads to
Rapid municipal industrial and electricity cooling demand
Growing deficit

## Slide 18: Challenges from Fracking
Between 2000 and 2014, water used to drill a horizontal natural gas well increased from 177,000 to 5.1 million gallons per well
Fracking (mining) is largest water use in some counties.
Heavy fracking in winter garden increased Carrizo-Wilcox drawdown.
Chart: Mining water usage as proportion of total usage
| 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Dimmit | 0.019043 | 0.022496 | 0 | 0.038067 | 0.017969 | 0.029532 | 0.033985 | 0.078539 | 0.079187 | 0.055077 | 0.060738 | 0.056735 | 0.059153 | 0.068403 | 0.0674 | 0.066725 | 0.00020336 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.010147 | 0.07557 | 0.14494 | 0.30403 | 0.47816 | 0.58322 | 0.58859 | 0.56907
LA Salle | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.01114 | 0.050118 | 0.096004 | 0.22253 | 0.46118 | 0.50611 | 0.64481 | 0.68403
Chart: Water Elevation of Well 7738103 on La Salle and Dimmit Boarder

## Slide 19: Existing Power Plants
51 Power plants in the research region
  10 solar power plants
  7 wind farms
  7 hydroelectric power plants
  4 biomass power plants
  4 coal power plants
  18 natural gas power plants
20 out of 22 fossil fuel power plants
in the research region used surface water for cooling
Plus there are 7 hydroelectric power plants
on Guadalupe River, but they don’t consume
the water
Chart: Power plant capacity percentage
| biomass | coal | natural gas | hydro | solar | wind
 | 27 | 3408.4 | 10910.6 | 22 | 236.7 | 1180.6

## Slide 20: Cooling Water Usage under different cooling methods
 | Water withdrawn and consumption (Gallons per MWh) |  |  |  |  |  | Construction cost per KW | Generation Cost per MWh | Fuel cost per MWh
 | Once-through |  | Recirculating |  | Dry-cooling |  |  |  | 
 | Withdrawal | Consumption | Withdrawal | Consumption | Withdrawal | Consumption |  |  | 
Coal (conventional) | 20,000 - 50,000 | 100 - 317 | 500 - 1,200 | 480 - 1,100 | N/A | N/A | $2934-6600 | $8-17 | ~$30
Natural gas (combined cycle) | 7,500 - 20,000 | 20 - 100 | 150 - 283 | 130 - 300 | 0 - 4 | 0 - 4 | $676-7108 | $5-43 | ~$41
Nuclear | 25,000 - 60,000 | 100 - 400 | 800 - 2,600 | 600 - 800 | N/A | N/A | $5530 | $12.79 | 
Source: Macknick, Jordan, Robin Newmark, Garvin Heath, and Kathleen C. Hallett. "Operational water consumption and withdrawal factors for electricity generating technologies: a review of existing literature." Environmental Research Letters7, no. 4 (2012): 045802. Summarized by Union of Concerned Scientists |  |  |  |  |  |  | EIA, https://www.eia.gov/outlooks/capitalcost/ |  | 

## Slide 21: Power Plant Retrofit
Boiler retrofit (coal to natural gas)
Cooling retrofit
  (Once-through to Recirculating to Dry-cooling)
Switch to renewable source: Wind and solar.
Add new capacity in or outside region
  Could export water use
  Wind and solar reliability are issue
Retrofit and new capacity cost will be in first stage of the model

## Slide 22: Cooling Retrofit Cost
 | Capital cost (once-through to recirculating) ($/kW) | Capital cost (once-through or recirculating to dry) ($/kW) | Capital cost (once-through to recirculating) ($/kW) | Capital cost (once-through or recirculating to dry) ($/kW) | O&M cost (once-through to recirculating) ($/kW/yr.) | O&M cost (once-through to dry) ($/kW/yr.) | O&M cost (recirculating to dry) ($/kW/yr.)
 | Average difficulty retrofits |  | Difficult retrofits |  | All retrofits |  | 
Coal | 90 | 220 | 140 | 330 | 2 | 5 | 3
Natural gas combined cycle | 40 | 170 | 65 | 270 | 2 | 10 | 8
Nuclear | 90 | 220 | 140 | 330 | 2 | 5 | 3
Biopower/biogas | 90 | 220 | 140 | 330 | 2 | 5 | 3
Oil/gas simple cycle | 90 | 220 | 140 | 330 | 2 | 5 | 3
Geothermal | N/A | 170 | N/A | 270 | N/A | N/A | 2
Concentrating Solar power | N/A | 170 | N/A | 270 | N/A | N/A | 2

## Slide 23
Projects

## Slide 24: WEF Alternatives – a starting point
Irrigation methods and practices Alternative crops
Ag Land to dryland or grazing Removing minimum limits
Degraded water use Crop mix
Dry year option
Water Use of more distant aquifers Injection &recovery
Reservoirs Saline sources
Enhanced recharge Conservation
Reuse Broader markets / leasing
Interbasin transfer
Energy Alternative cooling Coal to Natural Gas
Renewable sources wind solar Import more
Fracking water reuse Fracking technology

## Slide 25: Water Projects Examples
  Out-of-Region Water Project: Vista Ridge
  143 miles pipelines
  Yield: 50,000 acft/yr
  Water cost full operation $1,976 /acft
  Total cost of facility: $493 million
  Pumping Energy: 156,691 MWh/year
  ASR Project: Luiling ASR
  Total cost of facility: $23 million
  Annual cost of water: $1,086 / acft
  Energy Consumption for pumping: 1,617 MWh/year

## Slide 26: Public Goods Concern
Some Nexus actions will not be adopted by private individuals as they benefit the public not just the individual. In such cases the public will need to get directly involved in adoption.
Water Projects in our projects are public goods some ag possibilities are not

## Slide 27: Compensation Reallocation
When do we possibly need it?
  Suppose an entity like a Power plant could retrofit its cooling system to save water but don’t do it because its benefits are less than its cost
In such a case those benefitting possibly need to provide compensation to the power plants to increase their incentive to do the water saving retrofit.

## Slide 28
Modeling

## Slide 29: EDSIMR – the concept
Unify
  Detailed aquifer hydrologic model
  Regionalized economic Model
  Surface water flow model
  Hydrology embedded in regional economic model via regression (Keith Keplinger dissertation)
Keith O. Keplinger. "An investigation of Dry Year Options for the Edwards Aquifer. " Ph.D. Thesis, TAMU, 1996.
File Number 598 - Keplinger, K.O., and B.A. McCarl, "Regression Based Investigation of Pumping Limits and Springflow Within the Edwards Aquifer", Texas A and M University, 1995.
File Number 829 - Gillig, D., B.A. McCarl, and F.O. Boadu, "An Economic, Hydrologic, and Environmental Assessment of Water Management Alternative Plans for the South-Central Texas Region", Journal of Agricultural and Applied Economics, 33, 1 (April ), 59-78, 2001.

## Slide 30: EDSIMR “System” (and friends/ancestors)
Regional
Crop Mix
input use
Env.
loads
Crop and
Env
Simulators
(EPIC/SWAT)
Runoff
Simulators
(SWAT)
GIS
Non Ag
Resource
Demand
GCMs
Livestock
Data
Simulator Bundle
Pest
Regressions
Groundwater
Simulator
(GAM)
Water
Quality
EDSIMR
SWAT

## Slide 31: EDSIMR – Components Edwards Aquifer Groundwater and River System Simulation Model
What is contained in EDSIMR ?
Simulation Model (GAM)
Springflow, beginning/ending aquifer elevations, pumping
Econometric Model
Springflow/ending = f (beginning, recharge, pumping)
Mathematical Linear Programming
  Components : objective function
  : ag, M&I, power and fracking decision variable
  : constraints
  : Surface water Network flow
  : ground water characteristics
  Linkage : Ground Water + Surface Water

## Slide 32
State of Nature
Aquifers
(Edwards, Carrizo-Wilcox, Gulf Coast, Trinity)
Rivers (Nueces, Guadalupe, San Antonio)
Reservoirs (Canyon , Choke Canyon, Coleto Creek, Lake Corpus Christi, Medina Lake, Lake Texana)
Aquifer Diverters
River Diverters
Return Flows
Evaporation
Aquifer recharge, Depletion, Elevation
River Flows
Water Project Use (Exist and New)
Water Rights, & Markets
New Water Projects (Y/N)
Energy Retrofits
(Y/N)
Modeled Water Demand
Hydrological Processes
Investments
Reuse
Treatment Plants

## Slide 33
Cropland
Agricultural Water Use
Electrical Cooling Water
Fracking Water Use
Water Recreation
Hydro-Electric
Municipal Water
Industrial Water Use
Pasture&
Range
Crop Production
Livestock Production
Fresh water
Aquifer Diversion
River Diversion
Water Projects (Exist & New)
Brackish Water
Modeled Water Demand
Reuse
Return Flows
Treatment Plants
Treatment Plants
Environmental
Red means we are
Working on adding it

## Slide 34
Preliminary Results

## Slide 35: Power Plant Retrofit
Power Plant | Location | Retrofit
Coleto Creek | Goliad | Coal  NGCC
J. T. Deely | Bexar | Coal  NGCC
JK Spruce | Bexar | Coal  NGCC
San Miguel | Atascosa | Coal  NGCC
O.W. Sommers | Bexar | Recirculating  Dry
V.H. Braunig | Bexar | Recirculating  Dry
Barney | Nueces | Once Thru  Recirculating
Nueces Bay | Nueces | Once Thru  Dry
Penalties on once through
Other retrofits are on upstream of the river to save water

## Slide 36: Effects on Water Projects
Comparing with the model not forcing the inelastic demand of power plants cooling water, one water project is built and operated to support the increase demand of water.

## Slide 37: Effects on Water Costs
Water Source | Sector | Before ($/Acft) | After ($/Acft)
Surface | Agriculture | 10.6 | 10.6
Surface | Industrial | 1316.095 | 1439.283
Surface | Municipal | 1665.995 | 1826.492
Surface | Mining | 1898.065 | 1901.735
Ground | Agriculture | 12.39949 | 16.46617
Ground | Industrial | 1644.199 | 1584.059
Ground | Municipal | 1733.719 | 1713.315
Ground | Mining | 1950.404 | 1933.99

## Slide 38: Water Allocation
 |  | Before (Acft) | After (Acft)
Other Minor Aquifers | Industrial | 1677.248 | 2172.012
Other Minor Aquifers | Municipal | 44697.23 | 44720.9
Other Minor Aquifers | Mining | 3606.895 | 2517.664
Water Project | Municipal |  | 1174
Surface | Agriculture | 50238.41 | 64063.83
Surface | Industrial | 51772.6 | 14876.29
Surface | Municipal | 81857.28 | 27506.22
Surface | Mining | 4452.683 | 4674
Ground | Agriculture | 200742 | 203657.3
Ground | Industrial | 20976.1 | 25605.17
Ground | Municipal | 389464.2 | 444226.6
Ground | Mining | 44353.94 | 45221.85

## Slide 39: Conclusion
Power plant retrofit is a possible but expensive option to release water stress in the research region under FEW Nexus analysis.
The water projects will increase demand for electricity and generating more electricity will raise water demand.
The power plant surface water usage is not very responsive to price and it is likely more adjustment will be made in agricultural, industrial and municipal water plus switched to groundwater
Push up the price of water

## Slide 40: Future Research
Enhance the preliminary electricity part improving data and modeling on cooling alternatives and the use of electricity when developing the water projects
Considering the benefits of improved storage for wind and solar power plants
Consider water usage and reliability of power plants under climate change.
Add alternative strategies via which fracking can reduce its usage of fresh water.
Further consider means of compensation to incentivize power plant retrofit and the water projects

## Slide 41: Acknowledgement
This material is based upon work partially supported by the National Science Foundation under Grant Addressing Decision Support for Water Stressed FEW Nexus Decisions Numbered 1739977

## Slide 42
Thank you!